## Slide 1: Digital Logic Design
Lecture 01- 05

## Slide 2: Digital and Analog Quantities
Most natural quantities that we see are analog and vary continuously. Analog systems can generally handle higher power than digital systems. Digital systems can process, store, and transmit data more efficiently but can only assign discrete values to each point.
Many systems use a mix of analog and digital electronics to take advantage of each technology. A typical CD player accepts digital data from the CD drive and converts it to an analog signal for amplification
Digital electronics involves quantities with discrete values, and analog electronics involves quantities with continuous values. A digital quantity is one having a discrete set of values. Most things that can be measured quantitatively occur in nature in analog form.

## Slide 3: Digital and Analog Quantities
Analog and digital signals are the types of signals carrying information. The major difference between both signals is that the analog signals have continuous electrical signals, while digital signals have non-continuous electrical signals.
Digital circuits are more reliable. Digital circuits are easy to design and cheaper than analog circuits. The hardware implementation in digital circuits, is more flexible than analog. The occurrence of cross-talk is very rare in digital communication

## Slide 5: Digital and Analog Quantities

## Slide 7: Digital and Analog Quantities
Analog Quantities
photocopiers.
old land-line telephones.
audio tapes.
old televisions (intensity and color information per scan line)
VCRs (same as TV)
time, temperature, pressure, distance, and sound
Digital Quantities
Computers,
CDs,
DVDs
Smart Phones
The analog signal bandwidth is low | The digital signal bandwidth is high.

## Slide 8: Binary Digits, Logic Levels, and Digital
Because there are only two valid Boolean values for representing either a logic “1” or a logic “0”, makes the system of using Binary Numbers ideal for use in digital or electronic circuits and systems
In digital systems theses voltages are called “logic levels” and ideally one voltage level represents a “HIGH” state, while another different and lower voltage level represents a “LOW” state. A binary number system uses both of these two states

## Slide 9: Binary Digits, Logic Levels, and Digital
Digital electronics uses circuits that have two states, which are represented by two different voltage levels called HIGH and LOW.
The voltages represent numbers in the binary system.
VH(max)In binary, a single number is called a bit (for binary digit).
A bit can have the value of either a 0 or a 1, depending on if the voltage is HIGH or LOW.
HIGH VH(min)
Invalid VL(max)
LOW VL(min)

## Slide 10: Waveforms
Digital waveforms change between the LOW and HIGH levels. A positive going pulse is one that goes from a normally LOW logic level to a HIGH level and then back again. Digital waveforms are made up of a series of pulses.
Actual pulses are not ideal but are described by the rise time, fall time, amplitude, and other characteristics.
Periodic pulse waveforms are composed of pulses that repeats in a fixed interval called the period. The frequency is the rate it repeats and is measured in hertz. The clock is a basic timing signal that is an example of a periodic wave.

## Slide 17: Basic Logic Function
Digital logic has three basic operators, the AND, the OR and the NOT. These three operators form the basis for everything in digital logic. In fact, almost everything your computer does can be described in terms of these three operations

## Slide 25: Binary Arithmetic

## Slide 26: Complements of Binary Numbers

## Slide 27: Signed Numbers

## Slide 28: Arithmetic Operations with Signed Numbers

## Slide 30: Binary Coded Decimal (BCD)

## Slide 32: Digital Codes

## Slide 34: Even and Odd parity

## Slide 35: Computers and Electricity
Gate
A device that performs a basic operation on
electrical signals
Circuits
Gates combined to perform more
complicated tasks

## Slide 36: Computers and Electricity
How do we describe the behavior of gates and circuits?
Boolean expressions
Uses Boolean algebra, a mathematical notation for expressing two-valued logic
Logic diagrams
A graphical representation of a circuit; each gate has its
own symbol
Truth tables
A table showing all possible input value and the associated
output values

## Slide 37: Gates
Six types of gates
  NOT
  AND
  OR
  XOR
  NAND
  NOR
Typically, logic diagrams are black and white with gates distinguished only by their shape

## Slide 38: The Inverter
An inverter circuit outputs a voltage representing the opposite logic-level to its input. Its main function is to invert the input signal applied. If the applied input is low then the output becomes high and vice versa.

## Slide 39: NOT Gate
A NOT gate accepts one input signal (0 or 1) and returns the opposite signal as output
Figure 4.1 Various representations of a NOT gate

## Slide 40: AND Gate
An AND gate accepts two input signals
If both are 1, the output is 1; otherwise,
the output is 0
Figure 4.2 Various representations of an AND gate

## Slide 41: OR Gate
An OR gate accepts two input signals
If both are 0, the output is 0; otherwise,
the output is 1
Figure 4.3 Various representations of a OR gate

## Slide 42: XOR Gate
Figure 4.4 Various representations of an XOR gate
An XOR gate accepts two input signals
If both are the same, the output is 0; otherwise,
the output is 1

## Slide 43: XOR Gate
Note the difference between the XOR gate and the OR gate; they differ only in one input situation
When both input signals are 1, the OR gate produces a 1 and the XOR produces a 0
XOR is called the exclusive OR

## Slide 44: NAND Gate
The NAND gate accepts two input signals
If both are 1, the output is 0; otherwise,
the output is 1
Figure 4.5 Various representations of a NAND gate

## Slide 45: NOR Gate
Figure 4.6 Various representations of a NOR gate
The NOR gate accepts two input signals
If both are 0, the output is 1; otherwise,
the output is 0

## Slide 46: Review of Gate Processing
A NOT gate inverts its single input
An AND gate produces 1 if both input values are 1
An OR gate produces 0 if both input values are 0
An XOR gate produces 0 if input values are the same
A NAND gate produces 0 if both inputs are 1
A NOR gate produces a 1 if both inputs are 0

## Slide 47: Gates with More Inputs
Gates can be designed to accept three or more input values
A three-input AND gate, for example, produces an output of 1 only if all input values are 1
Figure 4.7 Various representations of a three-input AND gate

## Slide 48: Constructing Gates
Transistor
A device that acts either as a wire that conducts electricity or as a resistor that blocks the flow of electricity, depending on the voltage level of an input signal
A transistor has no moving parts, yet acts like a switch
It is made of a semiconductor material, which is neither a particularly good conductor of electricity nor a particularly good insulator

## Slide 49: Constructing Gates
A transistor has three terminals
  A source
  A base
  An emitter, typically connected to a ground wire
If the electrical signal is grounded, it is allowed to flow through an alternative route to the ground (literally) where it can do no harm
Figure 4.8 The connections of a transistor

## Slide 50: Constructing Gates
The easiest gates to create are the NOT, NAND, and NOR gates
Figure 4.9 Constructing gates using transistors

## Slide 51: Circuits
Combinational circuit
The input values explicitly determine the output
Sequential circuit
The output is a function of the input values and the existing state of the circuit
We describe the circuit operations using
  Boolean expressions
  Logic diagrams
  Truth tables

## Slide 52: Combinational Circuits
Gates are combined into circuits by using the output of one gate as the input for another

## Slide 53: Combinational Circuits
Three inputs require eight rows to describe all possible input combinations
This same circuit using a Boolean expression is (AB + AC)

## Slide 54: Combinational Circuits
Consider the following Boolean expression A(B + C)
Does this truth table look familiar?
Compare it with previous table

## Slide 55: Combinational Circuits
Circuit equivalence
Two circuits that produce the same output for identical input
Boolean algebra allows us to apply provable mathematical principles to help design circuits
A(B + C) = AB + BC (distributive law) so circuits must be equivalent

## Slide 56: Properties of Boolean Algebra

## Slide 57: Circuits as Memory
Digital circuits can be used to store information
These circuits form a sequential circuit, because the output of the circuit is also used as input to the circuit

## Slide 58: Integrated Circuits
Integrated circuit (also called a chip)
A piece of silicon on which multiple gates have been embedded
Silicon pieces are mounted on a plastic or ceramic package with pins along the edges that can be soldered onto circuit boards or inserted into appropriate sockets

## Slide 59: Integrated Circuits
Integrated circuits (IC) are classified by the number of gates contained in them

## Slide 60: Integrated Circuits
Figure 4.13 An SSI chip contains independent NAND gates

## Slide 61: CPU Chips
The most important integrated circuit in any computer is the Central Processing Unit, or CPU
Each CPU chip has a large number of pins through which essentially all communication in a computer system occurs

## Slide 62: The Exclusive-OR and Exclusive-NOR Gates

## Slide 63: Boolean Operations and Expressions

## Slide 64: Laws and Rules of Boolean Algebra

## Slide 65
De-Morgan’s Theorems

## Slide 66
Boolean Analysis of Logic Circuits

## Slide 67
Logic Simplification Using Boolean Algebra

## Slide 68
Standard Forms of Boolean Expressions

## Slide 69
Boolean Expressions and Truth Tables

## Slide 70
The Karnaugh Map